## Slide 2
Speakers
Pierre Daniel
Forecasting Operations Directorate, Marine and Oceanographic Forecasting Department, Météo- France
Vincent Gouriou
GIS Specialist, Information department, Cedre

## Slide 3
The Global Initiative for West, Central and Southern Africa (WACAF)
Angola
Benin
Cabo Verde
Cameroon
Congo
Democratic Republic of Congo
Equatorial Guinea
Gabon
Ghana
Guinea
Guinea-Bissau
Ivory Coast
Liberia
Mauritania
Namibia
Nigeria
Sao Tome and Principe
Senegal
Sierra Leone
South Africa
The Gambia
Togo
  Launch in 2006
  Objective
  Enhance the capacity of States to prepare for and respond to oil spills, so they can better protect their marine and coastal environment
  Technical assistance
    National and subregional workshops
    Trainings
    Exercises
    Conferences
  Annual budget:
    IMO
    Ipieca : 6 O&G companies
Notes: GI WACAF focuses on the Atlantic coast of Africa as you can see on the map and covers 22 countries. The main objective is to strengthen the capacity of the 22 partner countries to prepare for and respond to oil spills, to enable them to better protect their marine and coastal environment. To this end, we are implementing technical assistance activities. These activities consist of workshops, training (technical or legal) or table-top or deployment exercises.

## Slide 4
GI WACAF – OPRC Convention

## Slide 5: Drift modelling in oil spill preparedness and response at sea
28/06/2023
Pierre DANIEL (Météo-France) / Vincent GOURIOU (Cedre)

## Slide 6
Purpose of modelling tools (weathering and transport)
What information do you need for modelling ? (input data)
What are the main categories of models ?
Example of models (commercial software / opensource / institutional)
Demonstration : MOTHY
Demonstration : WEBGNOME
Choice and comparison of models (eg. French prediction committee)
The keys elements : environmental data
Limitations on modelling use
How to make a MOTHY request in the framework of MPERSS
Summary and conclusion
Presentation outline

## Slide 7
In case of an accident at sea, with the aim of defining a strategy, you need to anticipate:
The behaviour of the oil (weathering)
The drift of oil slicks (trajectory). Impacted shoreline.
As soon as possible and then regularly (recalibration with aerial, satellite and buoys observations).
Oilmap modelling (oil drift and behaviour)
Purpose of modelling tools (weathering and transport)

## Slide 8
Type of oil, properties (database)
  If you don't know the type of oil, you can also run the model drift (if possible : fill in the density)
Winds and currents
  In theory, oil moves at ± 3% of wind speed and 100 % of the current
In general, current is the most important parameter
Local, regional, global datasets
Wide variety of datasets through web servers / pay or free
Spill location, amount, etc.
Water temperature, salinity, sea state etc ...
What information do you need for modelling ? (Input data)

## Slide 9
There are different types of models :
Oil weathering models and especially evaporation, emulsification, dispersion, evolution of viscosity and density. For study and real case.
Trajectory or deterministic models are used to predict the route of an oil slick over time. Mainly for real case.
Stochastic models, which are also known as probability models, show the probability of where an oil spill may impact for defined time periods. Mainly for study.
Backtracking models, reverse the trajectory modelling process. These can be used to estimate the spill origin in situations where the source or release point is unknown. Mainly for study.
What are the main categories of models / which uses ?
Notes: Oil weathering models predict the changes in oil characteristics that may occur over time, under the influence of a variety of environmental conditions.
Trajectory or deterministic models are used to predict the route of an oil slick over time.
Stochastic models, which are also known as probability models, show the probability of where an oil spill may impact for defined time periods. Historical wind records that contain the frequency of wind speed and direction are required.
Backtracking models, reverse the trajectory modelling process. These can be used to estimate the spill origin in situations where the source or release point is unknown.

## Slide 10
Software with licenses, developed by private companies : OILMAP (RPS), OSCAR (SINTEF), MIKE (DHI), OSIS (BMT) …
Opensource / free models / institutional :
  WEBGNOME, ADIOS2 (NOAA, USA), online / worldwide
  Opendrift (Norwegian Meteorological Institute, Norway), software / opensource / worldwide https://opendrift.github.io
  MOTHY (Météo-France, France) in the framework of MPERSS, worldwide
  WITOIL (CMCC, Italy), online / worldwide http://witoil.com/app.html
What are the different models (software / opensource / institutional)
Notes: WITOIL :
http://www.witoil.com/
Noosdrift :
https://odnature.naturalsciences.be/noosdrift/

## Slide 11
OILMAP (RPS) - deterministic (real case and study)
OILMAP (RPS) provides predictions of the movement of spilled oil and its weathering
Notes: You can see the spill and the drift until the strandings on the shoreline during 48 hours simulation, you can also see the weathering model results with mass balance (graphics)
The oil weathering model predicts the changes in oil characteristics that may occur over time, under the influence of a variety of environmental conditions

## Slide 12: The use of ocean currents for oil spill monitoring
Stochastic model
(combination of 500 runs)
OILMAP (RPS) - stochastic (study)

## Slide 13: The use of ocean currents for oil spill monitoring
Probability of presence of the slick regardless of time
Minimum time to reach the coast
OILMAP (RPS) - stochastic (study)
Stochastic model
(combination of 500 runs)
Notes: This is a combination of 500 runs which provide the probability and the minimum time to reach the coast. On this map : some scenarios forecast some strandings in less than 12 hours
Stochastic models or probability models shows the probability of where an oilspill may impact for defined period, Historical wind and current records that contain the frequency of wind speed and direction are required,

## Slide 14
WEBGNOME (NOAA) (webgnome demonstration later)
WEBGNOME (NOAA) provides predictions of the movement of spilled oil and its weathering
1 - Download wind and current datasets : https://gnome.orr.noaa.gov/goods/
2 - Configure your scenario: https://gnome.orr.noaa.gov/ (manual setup)
1
2

## Slide 15
ADIOS 2 (NOAA) – weathering (webgnome demonstration later)
ADIOS Automated Data Inquiry for Oil Spills
Oil weathering model
NOAA (National Oceanic and Atmospheric Administration, USA)
FREE DOWNLOAD : http://response.restoration.noaa.gov/
Also available with Webgnome (cf. demonstration)

## Slide 16
ADIOS 2 (NOAA) – weathering (webgnome demonstration later)
Output data :
Overall budget
Evaporation
Emulsification (water content)
Dispersion
Viscosity
Density
Benzene concentration in air

## Slide 17
MOTHY system
        Surface/subsurface drift of hydrocarbons
        Since 1994
        Cargo container drift
        Since 1998
        81 SAR targets
        Since 2009
An emergency response service:
          Response time < 30 min
          H24 availability
          Global response capacity
Drift forecasts at Météo-France

## Slide 18
Over 1000 requests per year, 40 % for oil
2022
MOTHY drift forecasts
Over 1000 requests per year, 40 % for oil

## Slide 19
Oil drift forecasts examples

## Slide 20
MOTHY system

## Slide 21
Latest significant incident around Africa
25 July 2020: grounding of the bulk carrier Wakashio on a reef in Mauritius
Risk assessment for Réunion Island, 200 km to the west

## Slide 22
Additional features: backward drift
Searching for the origin of a pollution:
          which wreck is leaking?
          which ship has discharged gas?
          where is the wreckage of the plane that crashed?
Examples :
          EgyptAir flight 804 from Paris to Cairo crashed into the Mediterranean Sea on 19 May 2016.
          Backward drifts of debris and kerozene were used to locate the wreckage.
          This information was critical in determining the cause of the crash.

## Slide 23
Example :
          Wreckage risk analysis with hourly release for 30 years: 262,980 trajectory simulations.
Additional features: statistical trajectory analysis
Given a specific spill location, where might it go and what might it harm?
          Evaluate potential threats to sensitive locations from possible spill sites
          Identify shoreline areas that are likely to be impacted
          Calculate the likelihood of a certain amount of oil reach a given site within a specific timeframe
          Estimate the impact of a spill on a particular resource
          Analyze deficiencies in response personnel and equipment

## Slide 24
Quiz 1
(Quit full screen mode, check the chat !)

## Slide 25
Demonstration (MOTHY) - Angola
Request by e-mail
Specific form
Phone confirmation

## Slide 26
Demonstration (MOTHY) - Angola
Delivered on a dedicated website
Maps (GIF)
Animation (GIF)
Specific formats
    KMZ
    GPX
    SHP

## Slide 27: The use of ocean currents for oil spill monitoring
Demonstration (WEBGNOME)

## Slide 28: The use of ocean currents for oil spill monitoring
Demonstration (WEBGNOME)
Possibility of using your own datasets

## Slide 29: The use of ocean currents for oil spill monitoring
Demonstration (WEBGNOME)

## Slide 30: The use of ocean currents for oil spill monitoring
Demonstration (WEBGNOME)

## Slide 31: The use of ocean currents for oil spill monitoring
Demonstration (WEBGNOME)

## Slide 32: The use of ocean currents for oil spill monitoring
Demonstration (WEBGNOME) - Angola

## Slide 33: The use of ocean currents for oil spill monitoring
Webinaire ENG - Angola (MOTHY / WEBGNOME)
MOTHY
WEBGNOME
Scenario :
  2023/06/15 12:00:00
  1000 tons of Arabian light
  Instantaneous spill
  Location : 58 nautical miles from the Angola shoreline (7°S/12°30E)
  Simulation duration : 48 h
  Run with MOTHY (Météo-France). Winds : IFS / Currents : Copernicus
  Run with Webgnome (NOAA). Winds GFS / Currents : HYCOM

## Slide 34: The use of ocean currents for oil spill monitoring
Demonstration (WEBGNOME)

## Slide 35: The use of ocean currents for oil spill monitoring
Choice and comparison of models (ex : French prediction committee)
French Monitoring and Prediction Committee (for oil and chemical spill) is composed of Cedre, Météo-France, Ifremer, National Hydrographic service (SHOM) and state action at sea.
  Running and comparing the different models
  Comparing the same transport model with different datasets
  Comparing the transports models with each other
  Analyse the crisis situation and data using every output available from model
  Make operational recommendations
  Produce a synthetic map for broadcasting
  Sometimes : relationships with other countries (Prestige : Spain / France)
Notes:   The algorithms (oil drift calculation) may be different depending on the model
When there is a major incident as Prestige or Erika, a commitee with differents experts takes place every day
The committee runs differents model with different hydrodynamic input and then compares the results, then provides a common response to authorities, Sometimes : relationships with other countries (Prestige : Spain / France)
In that way and to respond to the challenge of a faster and better response, the secreteriat general of the sea create the drifting Committe on november 21 of 2002, during the prestige accident. This committee is a gathering of known scientists competent in oceanography, atmospheric dynamics and pollution domains. So during prestige it was composed of experts from Cedre, Meteo France, Ifremer, National Hydrographic service (SHOM) and state action at sea (which is in charge of managing the response at sea). The missions of the drifting committee are

## Slide 36
  FREE DATA : COPERNICUS https://marine.copernicus.eu/
  Provider: CMEMS (Copernicus Marine Environment Monitoring Service)
  Mercator PSY4 1/12° (GLOBAL Analysis Forecast Phy 001 024)
  Available in webgnome :
  Real-Time Ocean Forecast System (RTOFS) NOAA NWS/U.S. Navy 1/12 degree operational HYCOM)
  Hybrid Coordinate Ocean Model (HYCOM) HYCOM consortium multi-agency model https://www.hycom.org/
  PAID-FOR DATA :
  SATOCEAN(1/12°) Provider: SAT-OCEAN / based on HYCOM https://www.sat-ocean.com/
The key element : environmental data / Ocean current models

## Slide 37
  FREE DATA :
  ARPEGE (1/10° & 1/2°)
  Provider : Météo-France
  Coverage: Europe + worldwide
  https://donneespubliques.meteofrance.fr/
  GFS (1/4°) available in webgnome
  GLOBAL Forecast System
  Provider: NOAA NCEP
  National Centers for Environmental Prediction
  https://www.nco.ncep.noaa.gov/pmb/products/gfs/
  NAVGEM (1/2°)
  Navy GLOBAL Environmental Model
  Provider: U.S. Navy
  https://www.hycom.org/dataserver/navgem
The key element : environmental data / Atmospheric models
  PAID-FOR DATA : IFS (1/8°)
  ECMWF Integrated Forecasting System
  Provider: European Centre for Medium-Range Weather Forecasts
  Coverage: worldwide
  https://www.ecmwf.int/en/forecasts
  SAT-OCEAN (1/12°)
  Provider: SAT-OCEAN
  https://www.sat-ocean.com/

## Slide 38
  Near the shoreline, a river, an estuary
  In a harbour (specific study to create a complete current model, some weeks of work for oceanographers)
  Waves, turbulences, gales, oil weathering, interacting currents, local currents, differences of temperatures….
  Sometimes global currents are better than local currents
Limitation on modelling use / warning

## Slide 39
Marine Pollution Emergency Response Support System (MPERSS)
  A system coordinated by the World Meteorological Organization (WMO)
    In case of marine pollution emergency response operations :
    Provision of meteorological and oceanographic information
    Provision of drift forecasts
  Area concerned :
    Global
    Same geographical distribution than those for the Global Maritime Distress and Safety System (GMDSS)
    Outside waters under national juridiction
    For national waters at the request of the relevant countries

## Slide 40
MPERSS & GI WACAF area
  Assistance provided by:
    France over area II (from Mauritania to DRC)
    South Africa over area VII (Angola, Namibia and South Africa)

## Slide 41
  You provide your national meteorological service with the details of the marine pollution incident.
  The national meteorological service :
    Contact the Area Meteorological and Oceanographic Coordinator (AMOC)
    Either the French meteorological service (Météo-France)
    Or the South African Weather Service
  There is a specific procedure for this.
  The AMOC then provides forecasts of oil slick drift.
How to make a request in the framework of MPERSS ?

## Slide 42
Quiz 2
(Quit full screen mode, check the chat !)

## Slide 43
  WEBGNOME
    Datasets : https://gnome.orr.noaa.gov/goods/
    Configure your scenario: https://gnome.orr.noaa.gov/
ADIOS2 : http://response.restoration.noaa.gov/
MPERSS / MOTHY (http://www.meteorologie.eu.org/mothy/)
Tools exist, are useful provided you consider their limits
  Not magic, maths
  Validation on real cases
  Validation with buoys drifts / aerial and satellite observations
  Compare different models
  Discussions and expertise
Summary and conclusion